## Slide 1
Bottled Product Packaging
Seconds
Packaging
PROCESS STEP TIME BREAKDOWN  | Pick empty bottle from infeed tray | Feed bottle into labeling machine | Apply self-adhesive label | Visual quality check (label presence & alignment) | Manually correct label defects | Pack bottles into carton | Seal carton and place on conveyor | Apply shipping label | Total
VALUE-ADDED TIME | 2 | 3 | 4 | 0 | 0 | 5 | 3 | 2 | 19
PREPARATION TIME | 1 | 2 | 0 | 0 | 0 | 2 | 1 | 1 | 7
INSPECTION TIME | 0 | 1 | 2 | 3 | 1 | 1 | 1 | 1 | 10
FIXING ERRORS TIME | 0 | 0 | 1 | 0 | 4 | 0 | 0 | 0 | 5
REWORK TIME | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 3
WAITING TIME | 3 | 4 | 1 | 0 | 0 | 3 | 2 | 1 | 14
MOVEMENT TIME | 2 | 1 | 0 | 1 | 1 | 2 | 1 | 1 | 9
TOTAL | 8 | 11 | 9 | 4 | 8 | 13 | 8 | 6 | 
VA CLASSIFICATION | ENVA | ENVA | ENVA | ENVA | NVA | ENVA | ENVA | ENVA | 
SUGGESTED ACTION TYPE | Automate | Error-Proof | Automate | Automate | Eliminate | Reduce | Combine | Automate | 
IMPROVEMENT IDEAS | Install automatic bottle feeder to eliminate manual picking | Improve guide rails to reduce alignment adjustments | Upgrade label sensor to reduce misalignment and rework | Add vision system to automate inspection | Improve machine calibration to eliminate manual correction | Introduce auto-loader to reduce waiting & movement | Combine sealing & transfer station to reduce movement | Automate label printing at carton exit point | 
VA: Value-Added Activity
NVA: Non-Value-Added Activity
ENVA: Essential Non-Value-Added Activity
VA CLASSIFICATION: VA – NVA – ENVA
Notes: Value Analysis Matrix – © Copyright Continuous Improvement Toolkit . www.citoolkit.com

## Slide 2
Bottled Product Packaging
Seconds
Packaging
VA–NVA QUADRANT DIAGRAM
UNNECESSARY
NECESSARY
VALUE-ADDED
NON-VALUE-ADDED
Manually correct label defects
Pack bottles into carton
Pick empty bottle from infeed tray
Feed bottle into labeling machine
Seal carton and place on conveyor
Visual quality check (label presence & alignment)
Apply self-adhesive label
Apply shipping label
Notes: Value Analysis Matrix – VA–NVA Quadrant Diagram – © Copyright Continuous Improvement Toolkit . www.citoolkit.com